1967 NC HWY 69

Hayesville NC  28904.  (704) 796-3502

INSTALLATION INSTRUCTIONS – CONTROL ARMS/LONG ARMS

It is strongly advised that a professional mechanic install these parts.  It is the sole responsibility of the installer to know how to set the vehicle to all proper specifications, as improper installation will void your warranty.  IronMan Fabrication and 4X4 is not responsible for improper installation, lack of maintenance, abuse, and all other negligent acts leading to failure of any components based on improper installation of this product.

IMPORTANT:

- It is required that the installer torque jam nuts to 80 ft-lbs.

- Threadlocker such as Loctite Blue must be used with jam nuts.

- A minimum of 2” of threading must remain engaged in the upper arm. 3” for long arm joint.

READ ENTIRE INSTRUCTION SHEET BEFORE STARTING!

Long arm installation.

- Follow all factory manual instructions for proper location and jacking of vehicle.

- Mock up cross member first before installing any other parts. Properly support the transmission with a jack stand or trans jack.

- loosely bolt all mounting points on cross member and brackets for verification of location. Cross member can be mounted with the long arms mounting in front or behind cross member.

- Choose which location is better for your application and mark all mounting surfaces on sub frame for welding.

- Grind all welding surfaces before welding. PLEASE NOTE: THIS CROSS MEMBER MUST BE WELDED AS WELL AS BOLTED TO THE SUB FRAME. ANY FAILURE TO DO SO PROPERLY VOIDS THE ENTIRE CONTROL ARM WARRANTY.

- Weld the outer edge of both brackets to the frame as well as bolt with factory hardware. NOTE: If desired, drilling and tapping out factory holes to a 7/16 20 hole and using a grade 8 bolt increases the bolt strength of this cross member. This is not required but is suggested.

- After the mounting brackets have been installed and welded, mount and secure the cross member.

- Painting the brackets before installing is suggested.

- Install one long arm at a time. REMOVAL OF FACTORY LOWER CONTROL ARM BRACKETS MAY BE REQUIRED IN SOME APPLICATIONS.

- All bracket removal should be done professionally.

- Install long arms and set to desire locations.

- 90 degree and straight grease fittings are included for desired type to be used on long arm joint.

- USE YOUR HEAD! Installing these arms is not rocket science and can easily be done by a professional. If you are not a professional get some help from someone that is. Ironman4x4fab.com is in no way responsible for improper installation procedure and welding.

Here at IronMan we strive to provide quality and reliable parts that are an excellent value.  It is obvious that our prices are dramatically lower than our competitors.   We do powder-coat our control arms to provide a better level of endurance than paint would provide.  However, the coating is not warranted.  It is expected that the coating will become compromised under normal operation.

It is the sole responsibility of the installer to begin the routine maintenance and the user to continue maintenance of all these and all parts on a monthly basis.

All parts are not DOT approved, and are intended for off-highway use only, and must be set to all proper alignments and maintained in position.

Can I return orders?  YES!  However, you are responsible for return shipping.  Orders may be returned for warranty issues at any time without a restocking fee.  Non-warranty, unused condition orders may be returned within 60 days of receipt and are subject to a 15% restocking fee.  Non-warranty orders may not be returned after 60 days.

PLEASE NOTE:  Polyurethane bushings are designed for average to heavy-duty use. Exposure of the poly to extreme loads and extreme articulations can damage the bushings.  The bushings are not warranted for above-average use.  Flex joints are recommended for more extreme applications.