1967 NC HWY 69, Hayesville NC  28904.  (704) 796-3502

INSTALLATION INSTRUCTIONS – CONTROL ARMS

It is strongly advised that a professional mechanic install these parts.  It is the sole responsibility of the installer to know how to set the vehicle to all proper specifications, as improper installation will void your warranty.  IronMan Fabrication and 4X4 is not responsible for improper installation, lack of maintenance, abuse, and all other negligent acts leading to failure of any components based on improper installation of this product

IMPORTANT:

- It is required that the installer torque jam nuts to 80 ft-lbs.

- Threadlocker such as Loctite Blue must be used with jam nuts.

- A minimum of 1.250” of threading must remain engaged in the arm.

- Grease fittings monthly.

Here at IronMan we strive to provide quality and reliable parts that are an excellent value.  It is obvious that our prices are dramatically lower than our competitors.   We do powder-coat our control arms to provide a better level of endurance than paint would provide.  However, the coating is not warranted.  It is expected that the coating will become compromised under normal operation.

It is the sole responsibility of the installer to begin the routine maintenance and the user to continue maintenance of all these and all parts on a monthly basis.

INSTALLATION SUGGESTIONS:

- When installing a set of front control arms, it is suggested that the upper arms  be set 0.75” shorter than the lower arms as a good starting point.

- Lower control arms should be mounted with the bend oriented downward.

- Do NOT over grease the bushings.

Can I return orders?  YES!  However, you are responsible for return shipping.  Orders may be returned for warranty issues at any time without a restocking fee.  Non-warranty, unused condition orders may be returned within 60 days of receipt and are subject to a 15% restocking fee.  Non-warranty orders may not be returned after 60 days.

PLEASE NOTE:  Polyurethane bushings are designed for average to heavy-duty use. Exposure of the poly to extreme loads and extreme articulations can damage the bushings.  The bushings are not warranted for above-average use.  Flex joints are recommended for more extreme applications.

NOTE: YOU MAY NOTICE THE THREADS FEEL TIGHT AND ARE HARD TO TURN FOR ADJUSTMENT! THIS IS A GOOD THING! TIGHT THREADS = STRONG THREADS. FEEL FREE TO MOUNT THE BUSHING IN A BENCH VISE OR CONTROL ARM MOUNT AND TURN WITH A SCREWDRIVER ETC TO ACHIEVE DESIRED LENGTH. STATES WITH SALT MUST APPLY ANTI SEIZE TO AVOID INTERNAL SEIZURE.